## Slide 1: Large Pad GEM Beam Test in Hall D @ JLab
Kondo Gnanvo
EIC Weekly Meeting, Sepember 21, 2020

## Slide 2
Principe of large pads readout with high spatial resolution capabilities
2 large pads (1 cm2) share the initial charges: position from COG ⇨ expected similar or better performances in spatial resolution as X/Y strips with 100 pads instead of 512 for a XY readout
DLC layer
Dielectric: Kapton foil
Dielectric: Kapton foil
Dielectric: Kapton foil
Dielectric: Kapton foil
GND
DLC layer to evacuate the charges to the ground
Initial electron clouds size from triple GEM amplification will hit one pad of .6125 cm (average cluster size = 3 for a standard COMPASS XY R/O)
Readout pad 1 cm
Transfer pad 0.5 cm
Transfer pad 0.25 cm
Transfer pad 0.125 cm
Transfer pad 0.6125 cm
Stack of pad layers (5 layers for UVa prototype): 50 µm Kapton with 5 µm Cu pads ⇨ The pad size doubles (area × 4) from one layer to the layer underneath
Pad are arranged in space so that 2 neighboring pads of a given layers always partially share the same area with 2 neighboring pads on the layer underneath
Initial charges shared from one layer to the layer underneath through capacitive coupling (geometrical charge spread)
  Regardless size of bottom layer pads, at least always 2 pads see hits from initial charge cloud hits at least 2 pads of top layer
Only bottom pad layer is read out (readout layer) all the other layers on top participates only on the capacitive coupling charge spread (capacitive layers)
  Spatial resolution performances dictated in first order by the top layer pad size, independent of the bottom pad size
DLC layer on top of the first pad layer is mostly to evacuated the charges from the amplification but could contribute to the initial charge spread
  However DLC charge spread requires pad response function ⇨ so might requires some optimization to minimize its contribution to the charge sharing

## Slide 3
Beam test setup in Hall D @Jlab,
September 2020
e- (3-6 GeV)
GEM3
GEM2
GEM1
Large Pad GEM
Beam line
Electrons 3-6 GeV
Pair Spectrometer (PS)
gamma
e+
e-
Beam line
Large Pad GEM Telescope
One full week of data with 3 X-Y COMPASS GEM tracker and the large pad GEM
Hall D parasitic beam test with the Pair Spectrometer electron beam (3 to 6 GeV)
Data for HV scan of the large Pad GEM and for spatial resolution studies

## Slide 4
X-strips
Y-strips
X-strips
Y-strips
X-Pads
Y-Pads
X-strips
Y-strips
GEM1
GEM1
GEM2
GEM2
Pad GEM
Pad GEM
GEM3
GEM3
Preliminary results
(Plotted yesterday)

## Slide 5
Preliminary results
(Plotted yesterday)
GEM1
GEM2
Pad GEM
GEM3
Preliminary 2D Beam profile in X direction shows some non linearities compared to the X-Y strips detectors
Can be due to 3 causes know as limitations of the current prototype
  Pad size / resistive layer
  Inter Pad Gap (100 µm)
  Pad traces to the connectors (200 µm)

## Slide 6
New idea Capacitive sharing X-Y strip readout
For Triple GEMs
For µRWELL/micromegas